## Slide 1
HPCC: High Precision Congestion Control
Rui Miao
Yuliang Li, Hongqiang Harry Liu, Yan Zhuang, Fei Feng, Lingbo Tang, Zheng Cao, Ming Zhang, Frank Kelly, Mohammad Alizadeh, Minlan Yu
E6636BC20180234D78A0072836F0B330A2B9B20F15EA8B80AFD98931B16E2BB62B43B638616EAB0F223927083846ADEB9C1921FA11D03BD11BBFC2EC7E7E1BDA24F933AD172394E7F41D284767024E87EED2EBE67302D1E708EAF19A11202C38DD86259E4E3
Notes: As the name suggests, HPCC controls the congestion precisely, so it can maintain near-zero queue for ultra-low latency, while maintain very high throughput. Today Alibaba is actively deploying HPCC. Now let me introduce why we need HPCC, and how we design it.
25'

## Slide 2: High-performance networking is desired
High-performance storage
HDDSSDNVMe
Higher-throughput, lower latency
1M IOPS / 50~100us
CPUGPU, FPGA, ASIC
Faster compute, lower latency
E.g. latency <10us
Distributed deep learning
More network load
Need ultra-lower latency: 3-5us
E6636BC20180234D78A0072836F0B330A2B9B20F15EA8B80AFD98931B16E2BB62B43B638616EAB0F223927083846ADEB9C1921FA11D03BD11BBFC2EC7E7E1BDA24F933AD172394E7F41D284767024E87EED2EBE67302D1E708EAF19A11202C38DD86259E4E3
Resource disaggregation
compute
compute
compute
storage
storage
Network IO
network
C
C
C
M
M
M
G
G
G
M
Notes: [title], because the network -> the performance bottleneck in many systems in the cloud
New applications such as high-perf storage and large-scale distributed deep-learning, use new hardware that can generate and process data orders of magnitude faster than before, and allow very low access latency, so network is much more important than before.
Moreover, resource disaggregation is happening in the cloud, which disaggregate compute and memory into separate pools. So even memory accesses will go through the network, which adds considerable load to the network, and requires ultra-low latency. As a result, network is becoming bottleneck.
[]
Title of high per compute

## Slide 3: Two essential steps to high performance
E6636BC20180234D78A0072836F0B330A2B9B20F15EA8B80AFD98931B16E2BB62B43B638616EAB0F223927083846ADEB9C1921FA11D03BD11BBFC2EC7E7E1BDA24F933AD172394E7F41D284767024E87EED2EBE67302D1E708EAF19A11202C38DD86259E4E3
Network
App
Stack
NIC
App
Stack
NIC
App
Stack
NIC
Many ongoing efforts on hardware offloading
- RDMA, SmartNIC
More severe congestion
So Congestion control (CC) is very important!
CC
CC
CC
Notes: There are two essential steps toward high-performance networking. First, CPU cannot keep up with the high speed, so offloading the networking stack into the hardware is inevitable, and there are many recent efforts, such as RDMA and SmartNICs. Second, with the offloading, all the senders become faster, which cause even more severe congestion. So the congestion control is the [very important] for high-performance networking!
[]
Emphasize on CC. give transition from hw offloading to cc.
[]
Just leave the 2 sentences there
Talk about the title: CC is more important

## Slide 4: CC is immature in high-speed network
State-of-the-art CC in hardware-offloading solutions
  DCQCN[SIGCOMM 15]: ECN-based
  TIMELY[SIGCOMM 15]: delay-based
Face problems in operating large-scale RDMA networks
Root cause is the CC
Notes: [read]
Alibaba has a large-scale RDMA network
But, op face many problems in operating the network.
[read]

## Slide 5: Problems of state-of-the-art
Stability issues: incast/failure cause PFC storms or deadlock
Slow convergence
Challenge in reconciling BW-hungry app and latency-sensitive app
Standing queue
Parameter tuning takes months
CC parameters is hard to tune
Notes: They face stability issues, caused by PFC storm and deadlock
The root cause is [read], so buffer overflows frequently and trigger…
They face challenge in running [read] in the same cluster
the root cause is CC intentionally... to improve throughput, but it inflates the latency
parameter tuning is time consuming
the reason is [read]

## Slide 6: Problem 1: slow convergence
Operators’ problem
  Buffer overflow happens during incast/failure
    Use PFC to prevent loss: good performance on average, threat from PFC storm and deadlock
    Disable PFC: bad performance on average.
Root cause: CC cannot control the buffer well, because of slow convergence
  Imprecise feedback (ECN, delay) cannot tell the rate mismatch
  CC resolves congestion slowly, by halving the rate per RTT
  More severe in higher speed networks, because filling buffer faster
Ideally, adjust to the right rate in one RTT
  So loss is rare, and do not need PFC
Notes: In production, buffer overflows frequently during incast and failure, which are common events in DC
So operators PFC to prevent loss, which …
If you are not familiar with PFC, don’t worry, because they are just the result of buffer overflow.
The root cause is that CC cannot control buffer well because converge slowly
[]
Talk about our eval of not using pfc

## Slide 7: Problem 2: standing queues
Operators’ problem:
  Hard to run BW-hungry app and latency-sensitive app in the same cluster
Network
~5us base RTT
ML
ML
ML
Storage
Storage
>100µs latency
Notes: Standing queue cause long latency
In production, base RTT low, many app based on this assumption
But often complain high latency
In one case, ML …
Our investigation, standing q in net
Built by other BW hungry storage app.
7:20
[] add: operator’s problem

## Slide 8: Problem 2: standing queues
Root cause is CC
Feedback (ECN/delay) relies on the queue
CC intentionally keeps standing queues
Add 20~50us queueing delay
4~10x base RTT!!!
Notes: Key problem is, fdbk used today (ecn/d), rely on
Intentionally keep standing queue
What’s worse, operators set high queue, bcz [read]
The reason is, CC has rate fluctuations. When rate goes down, pkt in q keep link busy
If q is short, not enough pkt to keep link busy before rate goes up again, so lose thruput
So usuly op set high q, to keep link always busy
In DC, the rate fluctuation is even worse, bcz…
As a result, set very high, [read], up to 10 times …
Completely waste the ultra low base latency.
8:19
[]
Delete figure. Just keep standing q, and red text
Add cc problem

## Slide 9: Problem 3: complex parameter tuning
Tradeoffs
Many factors affect the tradeoffs
  Traffic patterns, failure scenarios, and network arch
Feedback (ECN/delay) is imprecise
  CC has to use heuristics to guess (1) network condition; (2) rate adjustments
Many parameters in such heuristics
  e.g., 15 parameters in DCQCN
  Tuning takes several months
Utilization
Stability
Throughput
Latency
Notes: [read title]
1st eg., op has to carefully tune, bcz [] requires more aggressive rate reduction, but more under-util
2nd eg, op has to carefully tune qlen, balance []and[]
In fact, op face [read]
Bcz these tradoff [read], but no [read] to tell CC what exactly they look like
So [read], e.g., dcqcn…
[and], precious rsrc, not available all time
[read]
[] heursitc: judge the current state of network, guess adjustment of rate,
[]
First show the rate adjustment, and queue len, then say they are funda tradeoff, show the upper part of figure
Many factors influence CC :
complex tuning:
many parameters,
tuning takes day/month, (say affect SLA…)

## Slide 10: Problems of state-of-the-art
Slow convergence
No precise feedback indicating how much to increase/decrease
Standing queue
Feedback relies on queue
Complex parameter tuning
No precise feedback  need heuristics: lots of parameters
One fundamental issue: coarse-grained feedback
What if we have precise feedback?
Notes: All 3 actually share same [read]
CC converges slowly [read]
There are standing queues [read]
Parameter tuning is complex [read]
So we ask, [read]
It turns out, just the right time to ask this question
10:20
[] feedback should not rely on queue

## Slide 11: HPCC: use INT as precise feedback
In-band network telemetry (INT) provides many details per packet
Broadcom&Barefoot have INT in recent products.
Widely used for diagnosis and monitoring in production
pkt
pkt
pkt
INT
INT
Sender
Receiver
Link-1
Link-2
Notes: Bcz a new type of feedback is available just recently
Big switch vendors such as [read]
In fact, [read], and this number is increasing with every new switch that they buy.
INT provides many detail per packet, such as qlen, and #tx bytes…
Every switch that enables INT, will push data to hdr… and later sw also append…, so receiver...
Alibaba is using INT for [read]. But, it has not been used for CC.
So a natural question is, [read]. To answer this question, we design HPCC.
11:23
[] Use separate slides for the popup
First talk INT, then vendor&productoin

## Slide 12
How good can CC do with INT as the feedback?
We design HPCC to answer this question

## Slide 13: HPCC solves the 3 problems
Slow convergence
No precise feedback indicating how much to increase/decrease
Standing queue
Feedback relies on queue
Complex parameter tuning
No precise feedback  need heuristics: lots of parameters
One fundamental issue: coarse-grained feedback
Using INT as the precise feedback
Fast convergence
Sender knows the precise rate to adjust to, on every ACK
Near-zero queue
Feedback does not rely on queue
Few parameters
Precise feedback, so no need for heuristics which requires many parameters
Notes: All 3 actually share same [read]
CC converges slowly [read]
There are standing queues [read]
Parameter tuning is complex [read]
So we ask, [read]
It turns out, just the right time to ask this question
10:20
[] feedback should not rely on queue

## Slide 14: HPCC: overview and challenges
ACK
Adjust rate
per ACK
Challenge 1: Feedback delay:
- Pkt/ACK may gets delayed
Challenge 2: Overreaction:
- Diff ACKs bring overlapping feedback
pkt
pkt
pkt
INT
INT
Sender
Receiver
Link-1
Link-2
Notes: 3 goals: [read]
achieves them as follows. When receiver, echoes back INT in ACK, so sender use as precise feedback, so that it knows the precise rate to adjust to
The sender react to every ack, adjust frequently
The goal of the adjustment is [read], so [read]
Also, precise fdbk, so no heuristic, so very few ..
But, 2 challenges:
[read], affect convergence speed
[read]
12:31
[] change to how precise fb achieves the 3 goals; del other two
Compare with slide 13. maybe in the same format even (or even 1 slides)

## Slide 15: Challenge 1: tolerate feedback delay
feedback
T
0
2T
Rate (DCQCN/TIMELY)
feedback
T
0
2T
No congestion
Congestion
High rate persists
Can be >> T
Because T is very low and
queueing delay dominates
(T is the base RTT )
HPCC
feedback
T
0
2T
Each sender use a window to limit inflight bytes: W=target_rate×T
Notes: [read title]
Recent HW-based CC (DCQCN and TIMELY) uses rate-based control. So they send pkt smoothly, and it is easy in hardware.
But it has problem. This is a no congestion case.
When cong, queue delay inflate RTT, so fdbk comes much later than T
Not only send for 1st T, but persistently send at a high rate, until fdbk comes. Much more damage during cong
In HPCC, [read], theoretically guaranteed enough
No cong, no impact
Cong, [read]. In this way, no matter how long fdbk delay is, bound the damage
But [read]. Unlike xx send at steady rate, hpcc may send a while and stops sending due to the win
[read]
14:42
[]
Red words should start with inflight
1 slide: rate on left, hpcc on right
2nd slide: left measure rate, right: cannot measure rate

## Slide 16: Challenge 1: tolerate feedback delay
feedback
T
0
2T
Congestion
feedback
T
0
2T
Need a new way of measuring congestion:
Rate-based scheme
Use rate mismatch
HPCC
Rate mismatch is bad measurement
Actual sending rate is non-constant, due to the inflight bytes limit
Notes: [read title]
Recent HW-based CC (DCQCN and TIMELY) uses rate-based control. So they send pkt smoothly, and it is easy in hardware.
But it has problem. This is a no congestion case.
When cong, queue delay inflate RTT, so fdbk comes much later than T
Not only send for 1st T, but persistently send at a high rate, until fdbk comes. Much more damage during cong
In HPCC, [read], theoretically guaranteed enough
No cong, no impact
Cong, [read]. In this way, no matter how long fdbk delay is, bound the damage
But [read]. Unlike xx send at steady rate, hpcc may send a while and stops sending due to the win
[read]
14:42
[]
Red words should start with inflight
1 slide: rate on left, hpcc on right
2nd slide: left measure rate, right: cannot measure rate

## Slide 17: Estimating inflight bytes
Use total inflight bytes to measure congestion
  Each flow needs to estimate the total inflight bytes
  Use INT to estimate the total inflight bytes
sender
B (bottleneck bandwidth)
T (base RTT)
Queue
congestion
No
Each sender estimates independently in a distributed way
Available in INT
Notes: In HPCC, measure cong based total [read], and the control law is also based on that.
single bottleneck as an eg to highlight key idea.
The network can be viewed as a pipe of …, where B is …, and T …. The pipe volume is B*T.
to know the extent of cong, each flow...
Which not only includes pkt of this flow, but also…
In this case, the … is within pipe volume, no congestion.
On the other hand, if …exceeds the pipe volume, pkt cannot fit will queue up. There is cong
Goal: [read], so no q, almost fully utilized
To converge quickly, how many times greater the .. Is, than the pipe volume
And each flow reduce win by k
For fairness, also…
Of course, rate is updated accordingly, proportional
Key question is, how INT estimate…
[]
From top to bottom
Use one case.
Add a sendtence on each flow calc independently and distributed
[]
Point 1: how to capture inflight
- Each flow just local view, so use INT to get global view
P2: how to computer win adjustment
- MIMD

## Slide 18: Controlling inflight bytes
Use total inflight bytes to measure congestion
  Each flow needs to estimate the total inflight bytes
  Use INT to estimate the total inflight bytes
Compute adjustment based inflight bytes
  Use MIMD to quickly adjust to the right rate
Notes: In HPCC, measure cong based total [read], and the control law is also based on that.
single bottleneck as an eg to highlight key idea.
The network can be viewed as a pipe of …, where B is …, and T …. The pipe volume is B*T.
to know the extent of cong, each flow...
Which not only includes pkt of this flow, but also…
In this case, the … is within pipe volume, no congestion.
On the other hand, if …exceeds the pipe volume, pkt cannot fit will queue up. There is cong
Goal: [read], so no q, almost fully utilized
To converge quickly, how many times greater the .. Is, than the pipe volume
And each flow reduce win by k
For fairness, also…
Of course, rate is updated accordingly, proportional
Key question is, how INT estimate…
[]
Point 1: how to capture inflight
- Each flow just local view, so use INT to get global view
P2: how to computer win adjustment
- MIMD

## Slide 19: Challenge 2: Fast reaction without overreaction
3
4
2
1
5
W=W0
/1.5
Ack1
Pipe volume=6
Per-ACK reaction
Overreaction

## Slide 20: Challenge 2: Fast reaction without overreaction
3
4
5
W=W0
/1.5
Ack1
Pipe volume=6
2
/1.3
Ack2
Overlap
overreaction
Per-ACK reaction
Overreaction

## Slide 21: Challenge 2: Fast reaction without overreaction
Per-ACK reaction
Overreaction
Per-RTT reaction
No overreaction
3
4
2
1
5
W=W0
/1.5
Ack1
Pipe volume=6
6
Next to react: 6

## Slide 22: Challenge 2: Fast reaction without overreaction
Per-ACK reaction
Overreaction
Per-RTT reaction
No overreaction
6
W=W0
/1.5
Ack1
Pipe volume=6
/1.1
Ack6
No overlap
no overreaction
Next to react: 6

## Slide 23: Challenge 2: Fast reaction without overreaction
Per-ACK reaction
Overreaction
Fast reaction to sudden bursts
Per-RTT reaction
No overreaction
Miss sudden bursts
W=W0
/1.5
Ack1
3
4
2
1
5
Pipe volume=6

## Slide 24: Challenge 2: Fast reaction without overreaction
Per-ACK reaction
Overreaction
Fast reaction to sudden bursts
Per-RTT reaction
No overreaction
Miss sudden bursts
HPCC combines per-ACK and per-RTT (details in paper)
No overreaction
Fast reaction to sudden bursts

## Slide 25: Theory proof
Asynchronized flows
Arbitrary topology
Convergence speed
Queueing delay
Fairness
Converge to Pareto optimal
Queue size is bounded
Max-min/proportional fairness

## Slide 26: Implementation
Commodity FPGA NIC
In a 32-server testbed

## Slide 27: Implementation in commodity FPGA NIC
14,000 lines of Verilog code for the whole NIC
2,000 lines for CC
  <2% of hardware resources
Optimization:
  look-up table: 8x speedup for division
  h/w friendly compression with <1% error: 10KB for [1, 4M]
  Multiple parallel engines: 6x more concurrent flows
INT header overhead: 4.2% (MTU=1KB)
Notes: We implemented HPCC in FPGA-based commodity NICs. The whole NIC takes 12000 lines, but the CC module only takes 2000 lines of them, and only uses <2% of all hardware resources. We also design many optimizations, including using look-up tables to speed up division by 8x. We also design h/w friendly compression of the look-up table, which just need 10KB to represent the range of 4M numbers. And we use multiple engines to support 6x more concurrent flows.
[]pkt size
22:31

## Slide 28: Implementation: testbed
Each server has two 25G FPGA NICs
32 servers
Notes: We use our NIC in our testbed. It has 32 servers, and each server has 2 NICs.
Please note this is just what we used when we submit the paper. Today Alibaba is actively developing and deploying HPCC in production.
22:51

## Slide 29: Evaluations
Setup
  32-server, 5-switch Testbed (25GE)
  320-server, 56-switch simulation, (100GE)
Traffic setting
  Web search, with diff levels of traffic load
  Hadoop, with diff levels of traffic load
  Diff incast sizes & ratios
  Many micro-benchmarks
Compare with DCQCN, TIMELY, DCTCP, with their recommended parameters
Metrics
  Flow completion time (FCT)
  Queue length distribution
Notes: We evaluate HPCC in both the testbed that we mentioned, and a larger scale simulation. We test many different traffic settings, including web search traffic and hadoop traffic, with different level of traffic load. And we also add different level of incast to those traffic, with different sizes and ratios. We also tested many micro-benchmarks. We compare with all production available CC, including DCQCN, TIMELY and DCTCP, with their recommended parameter settings. And we compare in terms of flow completion time, and switch queue length distribution. HPCC performs better in all scenarios.
23:34

## Slide 30: HPCC achieves lower FCT and near-zero queue
In testbed, vs. DCQCN (hardware-based, widely used in industry)
  Web search traffic at 50% load
Vs. other CC (unavailable in HW) in simulation. HPCC performs better
95% lower
55% lower
HPCC
- P99: 23KB (7us queue delay)
Notes: In our testbed, we show that HPCC reduces the flow completion time a lot. We compare with DCQCN, which is a hardware-based solution that is widely used in industry, and also widely deployed in Alibaba. HPCC performs better under many diff traffic patterns. For example, with web search traffic at 50% load, HPCC significantly reduces the tail FCT. Note that for long flows, HPCC and DCQCN performs similar; this is because they are less sensitive to queueing delay, and they occupy the bandwidth most of the time.
We also monitor the queue length distribution. HPCC achieves near zero queue. Even at 99pct, the queue length is only 23KB, which is only 7us queueing delay.
We also compare with other CC. They are not available in HW, so we compare in simulation. The result is similar. Refer to paper.
24:48

## Slide 31: HPCC has the potential to remove PFC
HPCC is persistently better, regardless of the flow control schemes
HPCC is insensitive to the flow control schemes
95 percentile FCT

## Slide 32: Conclusion
Collaborating with switch and NIC partners on
deploying HPCC in Alibaba’s production networks
Practical impact
Demonstrate problems of existing CC with real production experience
Implement HPCC with HW NIC & switch
Demonstrate using precise info from INT make CC highly performant
Address the challenge of using INT
Proof for convergence speed, queueing delay, and fairness
Advance in CC
Notes: The first of its kind.
We hope HPCC opens a window to next-generation CC in hardware-offloaded, high-speed networks.
27:10
[]
Regroup: into 2 groups
Check with Harry: MLX support HPCC, broadcom

## Slide 34: Difference with XCP
XCP adjust rate heuristically
   no clear physical meaning
HPCC
   total inflight bytes (clear physical meaning)

## Slide 35: txRate vs rxRate
rxRate is a overlapping term with qlen
  A high rxRate increases the queue occupancy  large qlen

## Slide 36: Multiple QoS queues?
Queue is a scarce resource in the cloud
  App has higher priority in using the queues (than network operator)
  Management/control plane traffic
  Diff CC mechanism
HPCC is complementary to using multiple-queue