## Slide 1: SilkRoad Making Stateful Layer-4 Load Balancing Fast and Cheap Using Switching ASICs
Rui Miao
James Hongyi Zeng, Jeongkeun Lee, Changhoon Kim, Minlan Yu
Notes: Today, I will present SilkRoad, where I will show how to leverage the programmability in emerging switching AISCs to build a fast and cheap layer-4 load balancer.

## Slide 2: Layer-4 Load Balancing
VIP1
Layer-4 load balancing is a critical function
  handle both inbound and inter-service traffic
  >40%* of cloud traffic needs load balancing (Ananta [SIGCOMM’13])
– Direct IP
– Virtual IP
DIP1
DIP2
DIP3
DIP4
DIP5
VIP1
DIP4
VIP2
L4 Load Balancer
Notes: L4 load balancer distributes the traffic for a service to a pool of servers.
Each service in the cloud is assigned with a virtual IP address. We call it VIP.
Each service is running on a pool of servers and each server has a direct IP address. We call it DIP.
For example, the request for VIP1 arrives at load balancer first and the load balancer selects DIP4 and then sends the request to the DIP4.
Layer-4 load balanacer is a critical function for cloud data centers,
because it handles not only the traffic from Internet coming into the cloud, but also the traffic across services within the cloud. Previous study has shown that more than 40% of cloud traffic needs layer-4 load balancing.
Next, I will talk about the challenges for building such layer-4 load balancer in cloud data centers.

## Slide 3
Scale to traffic growth
Multi-rooted topology
Datacenter transport
…
Cloud traffic has a rapid growth
  doubling every year in Google, Facebook (Jupiter Rising [SIGCOMM’15])
L2/L3: one big virtual switch
L4: can we scale out load balancing to match
the capacity of physical network?
Notes: Today, layer-4 load balancing becomes especially challenging because the amount of cloud traffic doubles every year.
And it means we require load balancing to not only handle the large traffic today, but also automatically scale out for the traffic growth in the future.
People have already scaled out L2/L3 functions, by treating data center fabric as one big virtual switch. Those works are ranging from multi-rooted topology design to datacenter transport for congestion control.
Building on top of the capacity provided by L2/L3 functions, can we scale-out L4 load balancing as well? This is the question we want to answer in SilkRoad.
“so that, as traffic grow, the service provider can easily increase their service capacity by simply adding more servers, without worrying about the load balancing could be a potential bottleneck.”

## Slide 4: Frequent DIP pool updates
VIP1
L4 Load Balancer
DIP pool updates
  failures, service expansion, service upgrade, etc.
  up to 100 updates per minute in a Facebook cluster
Hash function changes under DIP pool updates
  packets of a connection get to different DIPs
  connection is broken
Hash(p) % 3
ECMP: Hash(p) = 9
Hash(p) % 2
VIP1
Notes: To scale out, it sounds easy, because we can use ECMP at switches. ECMP naturally supports the traffic growth, but the essential challenge is the frequent DIP pool updates.
For example, when a connection arrives at L4 load balancer, asking for VIP1.
We run ECMP hashing on the header fields of the connection (like 5-tuples) to select a DIP.
Because we hash on the same header fields, all of packets of this connection will be forwarded to this DIP.
But, there is a problem because the DIP pool can change.
For example, with many devices, some of them may fail at any time. Operators may add servers for service expansion.
Service provider always wants to reboot servers to upgrade the service for adding new features, fixing bugs, and adding security patches.
We call those changes as DIP pool updates. [pause]. DIP pool updates are very common in a big data center.
In a Facebook cluster with 1000s of servers, we observe up to 100 DIP pool updates within in just a minute.
Under the DIP pool updates, the existing hash and the DIP assignment will change and some packets of a connection will get to a different DIP.
For example, here the same hash result 9 will mode 2 and the load balancer sends the packets to the second DIP.
Even a single packet of the connection is mis-delivered to a different DIP, the entire connection is broken. Because the connection lost the transport-layer state and application content.

## Slide 5: Per-connection consistency (PCC)
Broken connections degrade the performance of cloud services
  tail latency, service level agreement, etc.
PCC: all the packets of a connection go to the same DIP
L4 load balancing needs connection states
Notes: Broken connections can degrade the performance of cloud services.
When the connection is broken, all the transferred data is lost.
it allows only the application to restart a new connection, which usually takes a few seconds. Tail latency and service level agreement.
We really want to ensure this property and send all the packets of a connection to the same DIP. This is called per-connection consistency or PCC. To achieve that, the L4 load balancer needs to maintain the state for each connection.

## Slide 6: Design requirements
Scale to traffic growth
While ensuring PCC under frequent DIP pool updates
Notes: To summarize the design of building a layer-4 load balancing in cloud data centers,
Previous solutions cannot achieve both requirements at the same time.

## Slide 7: Existing solution 1: use software server
VIP1
High cost
  1K servers (~4% of all servers) for a cloud with 10 Tbps
High latency and jitter
  add 50-300 μs delay for 10 Gbps in a server
Poor performance isolation
  one VIP under attack can affect other VIPs
Software load balancer
Scale to traffic growth
PCC guarantee
Ananta [SIGCOMM’13]
Maglev [NSDI’16]
L4 Load Balancer
Notes: One solution commonly used in today’s data centers is to run layer-4 load balancing in software servers. We call them software load balancer.
Software load balancer has large DRAM to maintain connection states and guarantee PCC, but it cannot scale to traffic growth.
one data center has 10Tbps traffic. To handle such traffic, we need 1000 servers dedicated to run layer-4 load balancing, which accounts for around 4% of total physical servers in that data center. With the traffic doubling every year, we need more and more servers, which has a high cost.
Processing packets in software incurs a high latency, and with a high volume of traffic, this latency can vary between 50 to 300 us, even with the optimization like kernel bypassing. This latency matters for servicing the traffic across services within the cloud.
Last, a load balancer serves many VIPs. When one VIP is under attack, the other VIPs also get affected.
Those VIP experience latency increase and packet drops because of the poor performance isolation in software.
This is a critical challenge for many cloud data centers, because in a cloud with 100s of thousands of services, there are always some services under attacks at different times, and many other services get affected.

## Slide 8: Existing solution 2: partially offload to switches
Hash function changes under DIP pool updates
  switch does not store connection states
Scale to traffic growth
No PCC guarantee
VIP1
Duet [SIGCOMM’14]
Rubik [ATC’15]
ECMP: Hash(p) = 9
Hash(p) % 3
Partial offloading
Hash(p) % 2
Software load balancer
Notes: To scale to traffic growth, one idea is to offload L4lb to switches using ECMP functions. This partial offloading is proposed by previous works.
Recall that under DIP pool updates, the hash function and DIP assignment can change.
Because switch has no connection state, some packets of a connection can go to different DIPs, and this violates PCC.

## Slide 9: SilkRoad
 | Scale to traffic growth | PCC guarantee
Software load balancer |  | 
Partial offloading |  | 
SilkRoad |  | 
Challenge: guarantee PCC under multi-Tbps
Build on switching ASICs
with multi-Tbps
Address such challenges using hardware primitives
Notes: In summary, we talked about two previous works.
SLB can guarantee PCC but cannot scale to traffic growth.
Partial offloading can scale to traffic growth, but cannot guarantee PCC
We propose SilkRoad, which addresses such challenges using hardware primitives.
which achieves both scaling to traffic growth and PCC guarantee.
SilkRoad scales to traffic growth. because we use switching ASICs and it handles a full line rate of multi-Tbps traffic.
Under such high-speed, the big challenge is how to guarantee PCC.
Next, I will describe our design in detail.

## Slide 10: ConnTable in ASICs
VIP | DIP pool
20.0.0.1:80 | 10.0.0.1:20
 | 10.0.0.2:20
Connection | DIP
1.2.3.4:1234 20.0.0.1:80 TCP | 10.0.0.2:20
VIPTable
store the DIP pool for each VIP
ConnTable
store the DIP for each connection
Insert
miss
hit
1.2.3.4:1234
20.0.0.1:80 TCP
1.2.3.4:1234 10.0.0.2:20 TCP
Notes: In SilkRoad, we have a VIPTable, which store the DIP pool for each VIP. Like here xx
To ensure PCC across DIP pool updates, we introduce ConnTable to store the DIP for each connection.
In this example, the first packet of a new connection does not have an entry in ConnTable.
It goes to VIPTable where it runs a hash to select the second DIP. xx

## Slide 11: Design challenges
Challenge 2: do all the operations (e.g., PCC) in a few nanoseconds
Approach: use hardware primitives to handle connection state and its dynamics
Challenge 1: store millions of connections in ConnTable
Approach: novel hashing design to compress ConnTable
Notes: To implement this design in ASICs, we have two challenges.
First, ConnTable needs to store the entries for all active connections, which can be a few million in the cloud data centers.
To address that, we use novel hashing design to compress ConnTable, so that it can fit into the ASIC memory.
Second, under multi-Tbps, we only have a few nanoseconds to perform all the operations, such as ConnTable lookup, selecting a DIP in VIPTable, inserting a new entry into ConnTable to ensure PCC, etc.
that is challenging because the ASIC process all the packets in a pipeline, where in every cycle, there is a new packet coming in.
we cannot drop the packets and we cannot lock or stop the pipeline, either.
To address this challenge, our design leverages the hardware primitives in switching ASICs for our function operations such as handling connection state and its dynamics.

## Slide 12: Many active connections in ConnTable
Up to 10 million active connections per rack in Facebook traffic
  a naïve approach: 10M * (37-byte 5-tuple + 18-byte DIP) = 550 MB
ASIC features: storing all connection states just become possible
  increasing SRAM size
  emerging programmability allows to use SRAM flexibly
Year | 2012 | 2014 | 2016
SRAM (MB) | 10-20 | 30-60 | 50-100
Notes: Let’s look at challenge 1.
In Facebook traffic we studied, there are up to 10 M active connections in a top-of-rack switch.
To store those connections, a naïve approach is to store the 5 tuples and the selected DIP for each IPv6 connection.
It requires more than 500 MB memory.
Let’s look at how much memory provided in switching ASICs today.
ASIC SRAM increases a lot in recent years
and it reaches to 50-100 MB last year.
It just reaches the same order of magnitude of 500 MB we need. It is comparable now.
Traditional fixed function ASICs divide this SRAM into dedicated tables to support many functions. Most of those tables are not fully utilized and the memory is wasted.
Today, the switching ASICs become programmable now, which allows us to use SRAM flexibly.
For example, data center operator now can reduce the routing table size and completely remove MPLS table.
They can use the memory to build the exact functions they need.
We can use a large portion of SRAM for load balancing.
It is close but not enough.
Next, I will show our way to compress ConnTable to fit into ASIC SRAM.

## Slide 13: Approach: novel hashing design to compress ConnTable
Compact connection match key by hash digests
False positives caused by hash digests
  the chance is small (<0.01%)
  resolved via switch CPU (details in the paper)
Connection | DIP
0xEF1C | [1002:200C::1]:80
 | 
Connection | DIP
[2001:0db8::2]:1234[2001:0db8::1]:80 TCP | [1002:200C::1]:80
 | 
ConnTable
5-tuple
(37-byte)
hash digest
(16-bit)
Notes: We compress both the match field and action field in ConnTable.
To reduce match field, we use hash digest.
Instead of storing the 5 tuples of 37-byte for each connection, we store a hash digest with only saying 16 bits.
Using hash digests introduces false positives.
If two connections hash to the same digest in the same hash location.
We found that the chance of false positive is small. It is 1 out of 10k connections with 16-bit digest. We carefully detect and resolve all false positives using switch CPU with a small software overhead.

## Slide 14: Approach: compress ConnTable
Compact action data with DIP pool versioning
VIP | Version | DIP pool
[2001:0db8::1]:80 | 100000 | [1002:200C::1]:80
 |  | [1002:200C::2]:80
[2001:0db8::1]:80 | 100001 | [1002:200C::1]:80
 |  | 
DIPPoolTable
Connection | DIP
0xEF1C | [1002:200C::1]:80
 | 
Connection | Version
0xEF1C | 100000
0x1002 | 100001
 | 
ConnTable
18 bytes
version
(6-bit)
ConnTable
store VIP-to-DIP pool mapping
x 10M entries
Notes: Next, we compress the action field.
The action field stores the DIP, which is 18 bytes. Given that we have up to 10M entries, this takes a lot of memory.
Alternatively, we can also remember the VIP to DIP pool mapping, then we can simply run a hash over the DIP pool to select the same DIP.
But, we still need ConnTable, because this DIP pool can change.
So we introduce this DIPPoolTable and assign each DIP pool a version. We store the version for each connection in ConnTable.
Now a coming packet can get its version from ConnTable, then map the version to the actual DIP pool in DIPPoolTable. We then run a hash to select the same DIP.
When the DIP pool update happens, we simply assign a new version to the new DIP pool.
New coming connections now start to use the new DIP pool version, but existing connections are still mapped to the old DIP pool version in ConnTable. So the PCC is always guaranteed.
By using version , we reduce action field to saying 6 bits.
This memory saving in ConnTable is much greater than the additional memory used for maintaining DIPPoolTable, due to the difference in table size.
This is because a DIP usually serves for 1000s of active connections.

## Slide 15: Design challenges
Challenge 2: do all the operations (e.g., PCC) in a few nanoseconds
Approach: use hardware primitives to handle connection state and its dynamics
Challenge 1: store millions of connections in ConnTable
Approach: novel hashing design to compress ConnTable
Notes: Under Multi-Tbps, we only have a few nanoseconds.
The second challenge is how to finish all the operations I just described.

## Slide 16: Entry insertion is not atomic in ASICs
  ASIC feature: ASICs use highly efficient hash tables
  fast lookup by connections (content-addressable)
  high memory efficiency
  but, require switch CPU for entry insertion, which is not atomic
t1: Arrived
t2: Inserted
C1
1 ms
t
C1 is a pending connection between t1 and t2
match on ConnTable
to select DIP1
cannot see entry in ConnTable
select DIP1
Notes: Fortunately, ASICs have highly efficient hash tables. Those hash tables provide fast lookup by a given key like connections
Also high memory efficiency.
So if we allocate our ConnTable and DIPPoolTable in those hash tables, we can finish all the operations within a few nanoseconds.
However, there is an exception for entry insertion.
Those hash tables use a very compact data structure.
At the cost, inserting a new entry into those hash table requires a complex algorithm, which cannot be run in ASIC atomically.
So, the entry insertion is running in switch CPU and it takes time.
To give a concrete example,
Here shows the timeline of the connection C1, with its packets.
When the first packet arrives at t1, it selects DIP1.
But this connection can only be inserted into ConnTable at t2.
The gap is usually 1 ms in today’s switches.
Before t2, some packets of this connection cannot see the entry in ConnTable.
after t2 , All the following packets can match the entry in ConnTable to select DIP1 consistently.
During t1 and t2, the connection C1 is under the risk of violating PCC, so we call it as pending connection.

## Slide 17: Many broken connections under DIP pool updates
DIP pool update breaks PCC for pending connections
Frequent DIP pool updates
  a cluster has up to 100 updates per minute
Arrived
Inserted
use new version
and violate PCC
use old version
DIP pool update


1K connections
t
t
t
C1
Notes: The pending connection will be broken under the DIP pool update.
For example, when a DIP pool update happens, the first two packets have already selected a DIP from the old DIP pool version.
After the update, this following two packets will use the new DIP pool version and can select a different DIP. This violates PCC and the connection is broken.
We have not just one pending connection but many pending connections. Those connections arrived before the update but will only be inserted into ConnTable after the update.
All of those pending connection can be broken.
According to our study in Facebook traffic, there are up to 1k broken connections caused by just one DIP pool update.
Recall that we have up to 100 DIP pool updates in a minute, which causes up to 100K broken connections.

## Slide 18: Approach: registers to store pending connections
ASIC feature: registers
  support atomic update directly in ASICs
  store pending connections in registers
Arrived
Inserted
DIP pool update


t
t
t
Store in registers
Notes: To guarantee PCC for pending connections, our approach is to use registers which often used for counters.
Registers support atomic updates, where we can write the DIP selection for each connection into registers atomically.
So we can store all the pending connections in registers. By doing that, all the active connections are either stored in ConnTable or in registers. So the PCC is always guaranteed.

## Slide 19: Approach: registers to store pending connections
Strawman: store connection-to-DIP mapping
  to look up connections, need content addressable memory
  but, registers are only index-addressable
Key idea: use Bloom filters to separate old and new DIP pool versions
  store pending connections with old DIP pool version
  other connections choose new DIP pool version
  this is a membership checking, and only need index addressable
Details in the paper
Notes:   To store pending connections, a strawman solution is to store the connection-to-DIP mapping in registers just like in ConnTable.
  Like in ConnTable, this needs the lookup by a key (like a connection).
  However, the register only support the lookup by a given index.
Instead, our key idea is to use registers to build a Bloom filter, which requires only index lookup.
In the Bloom filter, we only store those pending connections using the old DIP pool version.
All other connections will miss bloom filter and choose the new DIP pool version.
In this way, we simplify the original key-value problem which needs key lookup,
into a membership checking problem which needs only index look up in bloom filter.
%Such simple Bloom filter needs index lookup, which match what registers provide.
“In addition, we use bloom filter only during the DIP pool update, so the number of registers we used is very small. “
Please check our paper for more details.

## Slide 20: Prototype implementation
Data plane in a programmable switching ASIC
  400 lines of P4 code
  ConnTable, VIPTable, DIPPoolTable, Bloom filter, etc.
Control plane functions in switch software
  1000 lines of C code on top of switch driver software
  connection manager, DIP pool manager, etc.
Notes: %We implement a connection manager for connection insertion and deletion, and Dip pool manager to perform DIP pool updates using bloom filter

## Slide 21: Prototype performance
Throughput
  a full line rate of 6.5 Tbps
  one SilkRoad can replace up to 100s of software load balancers
  save power by 500x and capital cost by 250x
Latency
  sub-microsecond ingress-to-egress processing latency
Robustness against attacks and performance isolation
  high capacity to handle attacks
  use hardware rate-limiters for performance isolation
PCC guarantee
Notes: Our prototype shows we can achieve full line rate
Accurate
Ask chang about latency

## Slide 22: Simulation setup
Data from Facebook clusters
  about a hundred clusters from PoP, Frontend, and Backend
  One month of traffic trace with around 600 billion connections
  One month of DIP pool update trace with around three millions update
Flow-level simulation
  run SilkRoad on all ToR switches
  16-bit digest and 6-bit version in ConnTable
Notes: To under SilkRoad performance over a large scale, we collect data from about a hundred Facebook datacenter clusters.
We studied three types of clusters.
PoP clusters receive direct requests from Internet users.
Frontend clusters receive the small number of requests from PoP clusters.
Backend clusters are runing Facebook internal services.
We collect both traffic trace and DIP pool update trace over a month.
We perform flow-level simulation by running SilkRoad on all ToR switches in each cluster.

## Slide 23: SilkRoad can fit into switch memory
switching ASICs have 50-100 MB SRAM
use up to 58MB SRAM
to store 15M connections
Notes: This figure shows the memory usage of SilkRoad across different clusters.
X-axis is the memory usage of SilkRoad in 99th percentile of time,
Y-axis shows the distribution across clusters
If we look at the tails of blue curve, the Backend cluster can have up to 15M connections.
SilkRoad uses 58 MB memory usage to store those connections.
Recall that switching ASICs today have 50-100 MB SRAM, we can fit SilkRoad into switch memory to serve the traffic for all the clusters.

## Slide 24: Conclusion
Application traffic
Application servers
SilkRoad: direct path
Scale to traffic growth with switching ASICs
High-speed ASICs make it challenging to ensure PCC
  limited SRAM and limited per-packet processing time
SilkRoad: layer-4 load balancing on high-speed ASICs
  a line rate of multi-Tbps
  ensure PCC under frequent DIP pool updates
  100-1000x saving in power and capital cost
Notes: Enable at
By eminilating software layers such as Software load balancing

## Slide 25
Thank You!
Please come and see our demo
  Implemented using P4 on Barefoot Tofino ASIC
  Time: Tuesday (August 22), 10:45am - 6:00pm
  Location: Legacy Room
Notes: Please come and see a working layer-4 load balancer on the real Barefoot Tofino ASIC today.

## Slide 26: Back up

## Slide 27: Network-wide deployment
Simple scenario: at all the ToR switches and core switches
  each SilkRoad switch announces routes for all the VIPs
  all inbound and intra-datacenter traffic is load-balanced at its first hop
VIP2
VIP1
DIP1
DIP2
DIP3
DIP traffic
VIP traffic
Core
Agg
ToR

## Slide 28: Network-wide deployment
Harder scenarios: network-wide load imbalance, limited SRAM budget, incremental deployment, etc.
Approach: assign VIPs to different switch layers to split traffic
VIP1
DIP1
DIP2
VIP1
DIP traffic
VIP traffic
VIP1
VIP assignment is a
bin-packing problem
Core
Agg
ToR
assign VIP1 to
Agg switches