## Slide 1
Rui Miao
Lingjun Zhu, Shu Ma, Kun Qian, Shujun Zhuang, Bo Li, Shuguang Cheng, Jiaqi Gao, Yan Zhuang, Pengcheng Zhang, Rong Liu, Chao Shi, Binzhang Fu, Jiaji Zhu, Jiesheng Wu, Dennis Cai, Hongqiang Harry Liu
E6636BC20180234D78A0072836F0B330A2B9B20F15EA8B80AFD98931B16E2BB62B43B638616EAB0F223927083846ADEB9C1921FA11D03BD11BBFC2EC7E7E1BDA24F933AD172394E7F41D284767024E87EED2EBE67302D1E708EAF19A11202C38DD86259E4E3
From Luna to Solar: The Evolutions of the Compute-to-Storage
Networks in Alibaba Cloud

## Slide 2: Alibaba Cloud -- Some Stats
Enabling Digital Transformations Around the World
Available Region
More than 2 million customers spanned across 200+ countries and regions
28 Regions & 85 Availability Zones
2800+ CDN Nodes, 150+ Tbps bandwidth
Massive storage -- 10s of exabytes & 10s of trillions of objects stored

## Slide 3: The compute-storage separation of EBS
Compute Cluster
Storage Cluster
Block
Server
Chunk
Server
Chunk
Server
Chunk
Server
Block
Server
● ● ●
● ● ●
Compute Server
Disk
● ● ●
vSwitch
VM1
Storage Agent (SA)
VMN
. . .
vSwitch
VM1
Storage Agent (SA)
VMN
. . .
Compute traffic
Compute Server
Storage traffic
Notes: Optimized independently
data safety, high utilization, and low cost
Fast application migration

## Slide 4: The compute-storage separation of EBS
Compute Cluster
Storage Cluster
Block
Server
Chunk
Server
Chunk
Server
Chunk
Server
Block
Server
● ● ●
● ● ●
Compute Server
Disk
● ● ●
vSwitch
VM1
Storage Agent (SA)
VMN
. . .
vSwitch
VM1
Storage Agent (SA)
VMN
. . .
Compute traffic
Compute Server
Backend Network
(BN)
Network becomes important for I/O operations
Storage traffic
Frontend Network
(FN)
Notes: Optimized independently
data safety, high utilization, and low cost
Fast application migration

## Slide 5: Traffic patterns
EBS takes ~60% DC traffic
Write: Read = 4:1
~40% of the flows are up to 4K bytes
EBS has high traffic volume, but is highly fan-out and latency sensitive

## Slide 6: Trend : kernel TCP cannot match SSD’s high-speed
Software (user-level TCP)
Hardware (RDMA)
Requirement
Scalability
Interoperability
Strong compatibility to connect different clusters
10K~100K of conns
Extensive inter-DC access
FN
BN
Scale up instead of scale out
Limit the failure domain
Consistent config within cluster
Notes: Best performance is not always

## Slide 7: LUNA: user-level TCP for EBS
80%
Across layer optimizations
  Run-to-complete with zero-copy
  Lock-free and share-nothing
Released ESSD in 2018
  1M IOPS and 100µs latency
  4 cores for 200Gbps w/ 4KB blocks
Lessons
  SA is becoming the bottleneck
  Software is unsustainable with the increasing speed
  Common network failures can be disasters to storage
4KB Read (95th percentile)

## Slide 8: Trend: the rise of bare-metal cloud
Flexibility
  No or custom virtual
  Custom H/W platform
Agility
  Limited overhead
  Lightweight and fast
Isolation and security
  Performance isolation
  No side-channel attacks
Dedicated hardware
Programmable hardware (ALI-DPU)
Bare-metal machine
Host
VM
VM
VM
VM
Cloud Infrastructure services
Compute
Network
Storage
Infra hardware
Cloud Infrastructure services
Compute
Network
Storage

## Slide 9: Challenges to EBS in bare-metal clouds
EBS has to run inside the ALI-DPU with resource constraint
PCIe to Host
Integrated PCIe
ALI-DPU
CPU
DMA
NIC
Memory
SA
LUNA
CPU overhead
Limited throughput

## Slide 10: Challenges to EBS in bare-metal clouds
SA has to run inside the ALI-DPU with resource constraint
DMA
NIC
ALI-DPU
CPU
Memory
SA
LUNA
Integrated PCIe
PCIe to Host
ALI-DPU
CPU
Memory
SA
Data path
Transport
Data Path
SA Control
Transport Control Plane
DMA
NIC
CPU overhead
Limited throughput
Ideal: offload EBS’s data path

## Slide 11: Solar: offload EBS’ data path
Goals:
  Hardware offloading to fit bare-metal architecture
  Path changing to actively avoid in-network failures  multi-path
Challenges:
  Both network stack and SA are complex and stateful
  Limited resources for scalability
  Hardware errors are common (e.g., bit flipping)

## Slide 12: The fusion of storage and network
Complexity comes from the overgeneralization and layered architecture
1
2
3
5
6
Blk1
Blk2
Conns & buffers
Blk3
Packet-to-block
Mapping
Storage Agent
Data blocks
Network stack
4
State for packet-to-block converting

## Slide 13: The fusion of storage and network
Complexity comes from the overgeneralization and layered architecture
1
2
3
5
Blk1
Blk2
Conns & buffers
Blk3
Packet-to-block
Mapping
Storage Agent
Data blocks
Network stack
4
State for packet-to-block converting
HoL blocking from In-order buffering
x
6

## Slide 14: The fusion of storage and network
Pkt1
Blk1
Blk2
Blk3
One-to-one
mapping
Data blocks (4KB)
Pkt2
Pkt3
Few states
Low packet buffer
Easy for multi-path
Bypass CPU and memory
Jumbo frames (4KB)
Pkt2
x
Complexity comes from the overgeneralization and layered architecture
13
1
2
3
5
Blk1
Blk2
Conns & buffers
Blk3
Packet-to-block
Mapping
Storage Agent
Data blocks
Network stack
4
State for packet-to-block converting
HoL blocking from In-order buffering
x
6

## Slide 15: READ request
Guest Memory
Metadata
Data
Host

## Slide 16: READ request
Guest Memory
FPGA
Metadata
Data
Host
QoS
CPU
ALI-DPU
Block
NVMe
READ
CMD

## Slide 17: READ request
Guest Memory
FPGA
Metadata
Data
Host
QoS
RPC
RPC ID | Pkt ID | Addr, Len
Rpc-0 | 0 | <0x0F, 4K>
Rpc-0 | 1 | <0x2F, 1K>
CPU
Addr
Entry
Polling
ALI-DPU
Block
NVMe
READ
CMD
Path & Congest. Control
READ Request
Addr
Addr table

## Slide 18: READ request
Guest Memory
Path & Congest. Control
FPGA
Metadata
Data
Host
Addr table
QoS
RPC
RPC ID | Pkt ID | Addr, Len
Rpc-0 | 0 | <0x0F, 4K>
Rpc-0 | 1 | <0x2F, 1K>
CPU
READ Request
Addr
Entry
Polling
ALI-DPU
Block
READ Response
NVMe
READ
CMD
UDP HDR
RPC HDR
EBS HDR
Data Block
(4K Bytes)
IP HDR
Packet (in)
CRC
Data Path
Addr

## Slide 19: READ request
Guest Memory
Decrypt
Path & Congest. Control
Addr
FPGA
Metadata
Data
Host
Addr table
QoS
RPC
RPC ID | Pkt ID | Addr, Len
Rpc-0 | 0 | <0x0F, 4K>
Rpc-0 | 1 | <0x2F, 1K>
CPU
CRC
READ Request
Addr
Entry
Data Path
Polling
ALI-DPU
CRC
Agg & Check
Block
READ Response
NVMe
READ
CMD
UDP HDR
RPC HDR
EBS HDR
Data Block
(4K Bytes)
IP HDR
Packet (in)
CRC
CRC Value

## Slide 20: Solar improves I/O performance
4KB Read (95th percentile)
40%

## Slide 21: Evolution of ESSD performance
Network stack reduced I/O latency by 72% and tripled the IOPS

## Slide 22: Lessons learnt
CPU is still loaded for running control plane
  Path selection, congestion control, etc., which can be intensive
Bypassing onboard PCIe will be a long-term requirement
  The key is to offload both network and application processing before DMA
Should reduce the risk of high latency brought by the jumbo frame
  Single flow: 4KB MTU ✕ 4 path / 10 µs = 12.8Gbps
  Require a fine-grained congestion control (e.g., HPCC (SIGCOMM’19))

## Slide 23: Thanks!